## Slide 1
Preliminary Design Review
XXX Team
CCP-XXX-PDR-XXXX

## Slide 2: Communications Systems
Data handling protocols
Data Downlinking Strategy
  TT&C Data Volume
  Payload Operation
Hardware
  Radiation Pattern Analysis
Link Budget
Frequency Licensing Status

## Slide 3: Communications Subsystems
EnduroSat type II transceiver data handling protocols:
Information | Transparent | AX.25
Maximum Information per payload (bytes) | 128 | 97
Minimum Information per payload (bytes) | 9 | 4
FEC correction | CRC | None
Overhead | Low | High
Standardization | No | Yes
ARQ | Yes | Yes
Notes: ARQ = Automatic Repeat Request
FEC = Forward Error Correction

## Slide 4: Communications Subsystems
For multiple ground stations and being flexible for other teams, AX.25 was chosen.
Information | Transparent | AX.25
Maximum Information per payload (bytes) | 128 | 97
Minimum Information per payload (bytes) | 9 | 4
FEC correction | CRC | None
Overhead | Low | High
Standardization | No | Yes
ARQ | Yes | Yes
Notes: ARQ = Automatic Repeat Request
FEC = Forward Error Correction

## Slide 5: Communications Systems
Operation:
  Endurosat type II transceiver, Half duplex
Protocol:
  AX.25
  Modulo 8 implementation
    7 Information frames before an acknowledge frame
  Information field: 776 bits of information (84.35%)
  Overhead: 144 bits (15.65%)

## Slide 6: Communications Systems
Network Layer Protocol (PID):
  Not implemented
Address:
  Determined by callsigns
Notes: https://www.tapr.org/pdf/AX25.2.2.pdf image taken from

## Slide 7: Communications Systems
Notes: Update name to Ukpik / add title of image acquisition Communication

## Slide 8: Communications Systems

## Slide 9: Communications Systems
Start I-Frame:
  Command for current transmission, maximum end transmission time ,Next time to transmit
  Next groundstation callsign
  Commands
    Send image thumbnails, send specific image, apply OBC patch, capture image
  Extreme case:
    Built in information frame for stop all transmission IMMEDIATELY.

## Slide 10: Communications Systems
TT&C I-Frame:
  First packet sent back by CubeSat
  Contains the following sensor information:
    OBC time
    GPS coordinates
    Sun Sensor Voltage + Currents
    Battery voltages
    Temperature Sensors
    Solar Panel voltages
    Magnetorquer current/voltage sensor
    Magnetic compass sensor
Notes: Time permitting go and check all the data yourself
Capture rate = 1 min
Sensors per 1 reading
General data ask vidushi

## Slide 11: Communications Systems
Acknowledge S-Frame (ARQ):
  Acknowledge send next frame
  Acknowledge do not send next frame
  Selective Reject a frame for retransmission
  Reject all frames, retransmit all

## Slide 12: Communications Systems
Taccess = Tstart_link + Tend_link + Tinformation
Uplink data rate = 1200bps
Downlink data rate = 9600bps
Where Tproc = process time ~50ms

## Slide 13: Communications Systems
VR Camera I-Frame
  Payload Operation
    Secondary provides thumbnail format for lower quality image to select
    Selection of full image via command by primary

## Slide 14: Communications Systems
Image provided by camera:
  Initial:
    Images captured in 12 bit JPEG
    3000 x 3000 pixels per image
    13.5MB per image
  Compressed:
    Up to 15x compression
    <1MB per image

## Slide 15: Communications Systems
Thumbnail generation:
  Bit depth: 12 bit  8 bit jpeg
  Reduce number of columns/rows by a factor (0.1)
12 bit jpeg, 1941 kB, FOV = 47
8 bit jpg, 4kB, FOV = 47

## Slide 16: Communications Systems
Hardware:
  Ukpik 1 Transceiver:
    Endurosat Type II UHF transceiver
    GMSK + FSK modulation
    Data rate: 1.2 kbps - 19.2kbps
    Half duplex
    Frequency range: 430-440MHz
    Output Power: 1W
    Noise Figure (LNA + filter insertion loss): 1.5dB

## Slide 17: Communications Systems

## Slide 18: Communication Systems
Hardware:
  Ukpik 1 Antenna:
  GOMspace 70 cm band Omnidirectional UHF CubeSat antenna
  Frequency range: 435
  LCHP forwards, RHCP backwards
  Peak gain 1.6dBi
  50
  30 g weight

## Slide 19: Communication Systems
Radiation Pattern Analysis:
  Information from GOMspace datasheet at 45

## Slide 20: Communication Systems
Work done by Kelsey Doerkson:
Additional information:
  Will be referring to monopole orientations in positive angle offsets.
  Referencing the substrate below
Datum

## Slide 21: Communications Systems
More information:
  45 degree offset of my model is more omnidirectional than ANT430 model from GOMspace
  The model makes an assumption of using perfect conductors for the monopoles
  Next steps: Add in the CubeSat structure to see the effects on the radiation pattern
  Bending was not done because it is unrealistic in ANSYS HFSS. Hands on testing more suitable

## Slide 22: Communications Systems
0 degrees:
  Max gain: 3.9 dB
  Min gain: -0.006dB

## Slide 23: Communications Systems
45 degrees:
  Max gain: 2.2 dB
  Min gain: -9.05dB

## Slide 24: Communications Systems
90 degrees:
  Max gain: 0.23dB
  Min gain: -0.007dB

## Slide 25: Communications Systems
Summary Chart for all monopole offsets simulated:
Monopole Offset (Degrees) | Maximum Gain (dB)
0 | 3.90
10 | 3.37
20 | 3.23
30 | 3.07
40 | 2.89
45 | 2.20
50 | 2.15
60 | 1.69
70 | 1.28
80 | 0.74
90 | 0.23

## Slide 26: Communication Systems
Groundstation Block Diagram
  Important Design Choices still:
    Filter design by capstone students
    Power amplifier gain
    Driven by: Third harmonic Output
    SDR transceiver specs.
      Etus USRB B210
    Link budget Output power need

## Slide 27: Communication Systems
Tight filtering needed
Moderate filtering needed

## Slide 28: Communication Systems
Link Budget:

## Slide 29: Communication Systems

## Slide 30: Communication Systems

## Slide 31: Communication Systems

## Slide 32: Communication Systems
Uplink Eb/No method chosen because SNR method has lacking information at this point of time.
Advice from Peter Kazakoff + outlined issues of Link Budget from July 31st 2019.
  Separating TX & RX when building ground station block diagram.
  Scaled back power from transmitter on earth
  Antenna noise temperature
    Adjusted CubeSat Noise temperature to gain-weighted average using ITU recommendations.

## Slide 33: Communication Systems
Antenna Noise Temperature:
  Ground station antenna still needs to be looked at. Conservative value of 530k chosen.
Cable loss was too high before, this has been scaled back to 0.85dB based on LM400 and 9m length.
Filter insertion losses added as an estimate 1 dB was added
Polarization switch was added in case of ADCS failure.

## Slide 34: Communication Systems
Frequency Licensing:
  Dr. Jayshri Sabarinathan and Nicholas Mitchell will be getting their amateur radio licenses.
  Required for RAC endorsement application
    Has been started but not completed
  Required for IARU satellite coordination request
    Has been started but not completed
  It is acknowledged that this will be the highest priority once PDR is over.

## Slide 35: AIT
~10 slides
Propose a design of the Electric Ground Support Equipment (EGSE);
Propose a design of the flatsat that will aid in the development of flight software and the verification of operations. Flatsat can be used for:
  Test and verify all hardware interfaces
  Verify all spacecraft modes and state transitions
  Test and verify software commands and procedures
  Validate Mission Operations commands and procedures
  Validate power transmission for operating modes
  Test for failure modes and recovery procedures
  Validate ground segment protocols and communications functionality
Propose CubeSat test plan including safety and handling procedure
Present the laboratory environment for spacecraft integration and tests