## Slide 1
Preliminary Design Review
Ukpik-1 Team
CCP-WAC-PDR-PPT1
PI: Jayshri Sabarinathan
PM: Matt Cross

## Slide 2: Mission Overview
Presented by Matt Cross

## Slide 3: Preface
Suffering from Success in Space!
  Assistant PM Matt Bourassa takes job at SED
  Systems team members Bryan, Alexis, Kelsey have internships at JPL
  Matt, Kelsey, Alexis, Chimira on LEAD science campaign
  Kelsey teaches short course at Paris Observatory, Chimira attends
  Alexis and Stephen have successful STRATOS balloon campaign
  Matt, Alexis, Lauren on LEAD cap-demo
High turnover with Capstone projects
  Students that have contributed to the preliminary design have moved on
  New capstone students just getting started on detailed design

## Slide 4: Preface
We acknowledge that gaps exist, and we will work towards filling those gaps

## Slide 5: Mission Objectives
The primary objective of Ukpik-1 is to provide experiential learning and training opportunities for students in spacecraft development and operations, and in STEM outreach program development and delivery.
The secondary objective is to integrate and operate an immersive VR camera in orbit for science and education.

## Slide 6: Requirements Nomenclature
“Must” denotes an externally imposed requirement
“Shall” denotes an internally imposed requirement subject to internal change
“May” denotes a goal requirement

## Slide 7: Mission Requirements
ID | Programmatic Requirements
MR-PR01 | The CubeSat program shall provide experiential learning opportunities in spacecraft systems throughout the project life
MR-PR02 | The CubeSat program shall support educational outreach program development and delivery
MR-PR03 | The CubeSat program shall comply with Western University’s health and safety standards
MR-PR04 | Must conform to CSA AIT HS guidelines
MR-PR05 | The CubeSat program must comply with the Canadian CubeSat Project Guidelines as outlined by the Canadian Space Agency
MR-PR06 | The CubeSat program must comply with the project schedule as specified by the Canadian Space Agency
MR-PR07 | The CubeSat program must comply with the launch requirements as set by the launch provider
MR-PR08 | The CubeSat program must comply with ground safety requirements as set by the launch provider
MR-PR09 | The CubeSat program shall facilitate student engagement with the Nunavut Arctic College on the CubeSat project

## Slide 8: Mission Requirements
ID | Science and Outreach Requirements
MR-SC01 | The CubeSat shall integrate an immersive VR camera as a primary science and outreach payload
MR-SC02 | The CubeSat may integrate an accelerometer as a secondary payload for space weather events as a goal
MR-SC03 | The CubeSat shall acquire and return to ground at minimum 5 images of either scientific or outreach interest from the VR camera
MR-SC04 | The CubeSat may solicit public input for image target selection as a goal
MR-SC05 | The acquired VR images shall be made publicly available
MR-SC06 | The acquired VR images and video shall me viewable with an Oculus Rift
MR-SC07 | The acquired VR images may be viewable with other VR headsets as a goal
MR-SC08 | The CubeSat may acquire images at a rate of 5 per week as a goal
MR-SC09 | The CubeSat may acquire 1 VR video as a goal
MR-SC10 | The CubeSat may image the moon as a goal
MR-SC11 | The CubeSat may image the Northern Canada as a goal
MR-SC12 | The CubeSat may image the limb of the Earth as a goal
MR-SC13 | The CubeSat may image the atmosphere as a goal

## Slide 9: Mission Requirements
ID | Operational Requirements
MR-OP01 | The CubeSat must operate in a Low Earth Orbit as determined by the launch provider
MR-OP02 | The CubeSat shall be primarily operated by Western University students
MR-OP03 | The CubeSat may be operated remotely through an internet-based operations console
MR-OP04 | The CubeSat shall operate for a baseline mission of 6 months
MR-OP05 | The CubeSat may operate for more than 6 months as a goal
MR-OP06 | The CubeSat must adhere to Nanoracks BOL LEOP requirements
MR-OP07 | The CubeSat may turn on camera upon deployment from ISS as a goal
MR-OP08 | The CubeSat must comply with EOL requirements
MR-OP09 | The CubeSat must comply with communications licensing policies
MR-OP10 | The CubeSat must comply with remote sensing licensing policies
MR-OP11 | The CubeSat must conform to Controlled Goods licensing
MR-OP12 | The ground station must have the proper licensing
MR-OP13 | The CubeSat shall utilize available ground station infrastructure
MR-OP14 | The CubeSat shall log telemetry for mission operators

## Slide 10: Spacecraft Operational Modes
Mode | Transitions From | Description | Transitions To
Launch |  | All systems remain off | Deployment Mode
Deployment | Launch Mode | Triggered by deployment switches; initiates 30 minute timer | Safe Mode
Safe | Any | Reboots on board computer | Detumble
Detumble | Safe | Identifies current rotation rate and then reduces rate to point solar panels towards sun | Nominal, Safe
Nominal | Detumble, Imaging, Transmission, Eclipse | Controlled attitude, charging batteries, processing time-tagged queue | Imaging, Transmission, Eclipse, Safe
Imaging | Nominal | Switches on cameras, takes images as requested, facilitates data transfer from camera memory to OBC, draws power from battery | Nominal, Safe
Transmission | Nominal | Draws power from battery to transmit to ground | Nominal, Safe
Eclipse | Nominal | Reduced power consumption, draws power from battery | Nominal, Safe

## Slide 11: Concept of Operations
1 Primary ground station (London area)
  ~7 ground station passes
  Receive TM and Images at every opportunity
  Send time-tagged queue of TC
Secondary GS for receiving (as available)
Remote Mission Control to permit operations ‘in the classroom’
Immersive image display for public outreach

## Slide 12: Concept of Operations
Capture images of deployment from ISS (if permitted)
Solicit imaging requests from public, with priority to Nunavut Arctic College requests
Generate 7-day time tagged queue of TC, updated daily
Onboard image quality assessment, downlink low-res thumbnails
Downlink higher-quality images

## Slide 13: System Requirements – Payload
 | Payload Requirements
SY-PA01 | The VR cameras shall have a bill of materials to provide the launch provider
SY-PA02 | The VR cameras may switch on upon deployment from ISS as a goal
SY-PA03 | The VR cameras shall be operable on a time-tagged queue
SY-PA04 | One image shall be two semi-spherical images stitched together on the ground
SY-PA05 | The CubeSat shall integrate an Inuit engraving

## Slide 14: Inuit Engraving
Requirement to provide mass and volume allocation, and mounting bracket for an Inuit engraving supplied by Nunavut Arctic College students
Intention is for NAC to utilize material sourced from Nunavut
Initiates Fall 2019

## Slide 15: Systems Engineering
Presented by Nick Mitchell

## Slide 16: Internal Hardware Layout

## Slide 17: Space to Ground Interfaces

## Slide 18: Power Interfaces

## Slide 19: Communications Interfaces

## Slide 20: System Requirements (Overview)
ID | Space Segment Requirements
SY-SS01 | The CubeSat shall be a 2U form factor
SY-SS02 | The CubeSat must comply with NanoRacks deployment specifications
SY-SS03 | The CubeSat must have a remove before flight pin
SY-SS04 | The CubeSat must have deployment switches
SY-SS05 | The CubeSat must have a 30-minute timer circuit
SY-SS06 | The CubeSat must provide a bill-of-materials to NanoRacks
SY-SS07 | The CubeSat must comply with outgassing specifications
SY-SS08 | The CubeSat shall receive and execute time-tagged telecommands
SY-SS09 | The CubeSat shall transmit time-tagged telemetry
SY-SS10 | The CubeSat shall determine its pose
SY-SS11 | The CubeSat shall control its pose
SY-SS12 | The CubeSat shall determine its orbital position
SY-SS13 | The CubeSat shall provide enough power to operate all mission modes throughout its mission life
SY-SS14 | The CubeSat shall survive the test environment
SY-SS15 | The CubeSat shall survive the integration environment
SY-SS16 | The CubeSat shall survive the launch environment
SY-SS17 | The CubeSat shall survive the low earth orbit thermal environment
SY-SS18 | The CubeSat shall survive the low earth orbit radiation environment
SY-SS19 | The CubeSat shall facilitate integration of two Canadensys NISA cameras
SY-SS20 | The CubeSat shall facilitate transmission of images from the camera to the ground
SY-SS21 | The CubeSat shall safely re-enter atmosphere and burn up
SY-SS22 | The CubeSat must have a launch mass less that 3.6kg
SY-SS23 | The CubeSat shall be operated in a LEOP & Checkout phase and a nominal phase
SY-SS24 | The CubeSat and its components shall be designed and manufactured to meet system requirements for a minimum operational lifespan of 6 months
SY-SS25 | The CubeSat components shall be designed or selected to prevent undesired electromagnetic effects

## Slide 21: System Requirements (Overview)
SY-SS26 | The CubeSat shall always be in one of the following operations: Launch Mode; Deployment Mode; Detumble Mode; Safe Mode; Eclipse Mode; Communications Mode; Imaging Mode; and Nominal Mode
SY-SS27 | The CubeSat shall be delivered to the launch provider in Launch Mode
SY-SS28 | The CubeSat shall exit Launch Mode into Deployment mode upon deployment from ISS
SY-SS29 | The CubeSat transition to Deployment Mode shall trigger a 30 minute timer.
SY-SS30 | The VR cameras may switch on to begin imagining during Deployment Mode as a goal
SY-SS31 | The CubeSat shall deploy its antenna following the 30 minute delay
SY-SS32 | The CubeSat shall bootup the OBC during Deployment Mode
SY-SS33 | The CubeSat shall exist Deployment Mode into Detumble Mode following the antenna deployment
SY-SS34 | The CubeSat shall minimize its initial rotation rates during Detumble Mode
SY-SS35 | The CubeSat shall control its pose to face its solar panels towards the sun during Detumble Mode
SY-SS36 | The CubeSat shall respond to TC with TM during Detumble Mode
SY-SS37 | The CubeSat shall exit Detumble Mode into Nominal Mode through TC
SY-SS38 | The CubeSat shall enter Safe Mode either through TC or through detection of an onboard anomaly
SY-SS39 | The CubeSat shall exit Safe Mode into Detumble Mode through TC
SY-SS40 | The CubeSat shall enter Imagining Mode through time-tagged TC
SY-SS41 | The CubeSat shall exit Imaging Mode into Nominal Mode through time-tagged TC
SY-SS42 | The CubeSat shall enter Communications Mode through time-tagged TC
SY-SS43 | The CubeSat shall exit Communications Mode into Nominal Mode through time-tagged TC
SY-SS44 | The CubeSat shall enter Eclipse Mode either automatically or through time-tagged TC
SY-SS45 | The CubeSat shall exit Eclipse Mode into Nominal Mode either automatically or through time-tagged TC
SY-SS46 | The CubeSat shall function autonomously for a maximum of 7 days without intervention from MC
SY-SS47 | The CubeSat shall detect onbaord anomalies
SY-SS48 | The CubeSat shall provide pointing accuracy of 15 degrees for the solar panel aligned with the normal to the sun vector
SY-SS49 | The CubeSat shall have a centre of mass within 2cm of the of centre of volume
SY-SS50 | The CubeSat configuration shall be such that no unit be subjected to loading beyond the limits stated in its specification
SY-SS51 | The CubeSat shall store up to 10 days of housekeeping data as a minimum
SY-SS52 | The CubeSat flight software shall be reprogrammable in orbit
SY-SS53 | The CubeSat power system shall be sized for an expected EOL of 12 months
SY-SS54 | The CubeSat system shall be designed for ground-based testability
SY-SS55 | The CubeSat system shall be designed with ease of assembly and integration in mind

## Slide 22: Single Point Failures
Deployment switches don’t activate timer and CubeSat never switches on
OBC does not boot properly

## Slide 23: Single Point Impediments
Antennae do not deploy fully resulting in reduced gain; can possibly still downlink 5 images
Magnetorquers fail; communications or imaging do not require pointing, reduced power generation for battery charging reduces transmission of images

## Slide 24: Communications Systems
Work done by Nick Mitchell, Kelsey Doerksen, 2018/2019 Capstone Teams
Work presented by Nick Mitchell

## Slide 25: Communications Systems
Data handling protocols
Data Downlinking Strategy
  TT&C Data Volume
  Payload Operation
Hardware
  Radiation Pattern Analysis
Link Budget
Frequency Licensing Status

## Slide 26: Communications Subsystems
EnduroSat type II transceiver data handling protocols:
Information | Transparent | AX.25
Maximum Information per payload (bytes) | 128 | 97
Minimum Information per payload (bytes) | 9 | 4
FEC correction | CRC | None
Overhead | Low | High
Standardization | No | Yes
ARQ | Yes | Yes
Notes: ARQ = Automatic Repeat Request
FEC = Forward Error Correction

## Slide 27: Communications Subsystems
For multiple ground stations and being flexible for other teams, AX.25 was chosen.
Information | Transparent | AX.25
Maximum Information per payload (bytes) | 128 | 97
Minimum Information per payload (bytes) | 9 | 4
FEC correction | CRC | None
Overhead | Low | High
Standardization | No | Yes
ARQ | Yes | Yes
Notes: ARQ = Automatic Repeat Request
FEC = Forward Error Correction

## Slide 28: Communications Systems
Operation:
  Endurosat type II transceiver, Half duplex
Protocol:
  AX.25
  Modulo 8 implementation
    7 Information frames before an acknowledge frame
  Information field: 776 bits of information (84.35%)
  Overhead: 144 bits (15.65%)

## Slide 29: Communications Systems
Network Layer Protocol (PID):
  Not implemented
Address:
  Determined by callsigns
Notes: https://www.tapr.org/pdf/AX25.2.2.pdf image taken from

## Slide 30: Communications Systems
Notes: Update name to Ukpik / add title of image acquisition Communication

## Slide 31: Communications Systems

## Slide 32: Communications Systems
Start I-Frame:
  Command for current transmission, maximum end transmission time ,Next time to transmit
  Next groundstation callsign
  Commands
    Send image thumbnails, send specific image, apply OBC patch, capture image
  Extreme case:
    Built in information frame for stop all transmission IMMEDIATELY.

## Slide 33: Communications Systems
TT&C I-Frame:
  First packet sent back by CubeSat
  Contains the following sensor information:
    OBC time
    GPS coordinates
    Sun Sensor Voltage + Currents
    Battery voltages
    Temperature Sensors
    Solar Panel voltages
    Magnetorquer current/voltage sensor
    Magnetic compass sensor
Notes: Time permitting go and check all the data yourself
Capture rate = 1 min
Sensors per 1 reading
General data ask vidushi

## Slide 34: Communications Systems
Acknowledge S-Frame (ARQ):
  Acknowledge send next frame
  Acknowledge do not send next frame
  Selective Reject a frame for retransmission
  Reject all frames, retransmit all

## Slide 35: Communications Systems
Taccess = Tstart_link + Tend_link + Tinformation
Uplink data rate = 1200bps
Downlink data rate = 9600bps
Where Tproc = process time ~50ms

## Slide 36: Communications Systems
VR Camera I-Frame
  Payload Operation
    Secondary provides thumbnail format for lower quality image to select
    Selection of full image via command by primary

## Slide 37: Communications Systems
Image provided by camera:
  Initial:
    Images captured in 12 bit JPEG
    3000 x 3000 pixels per image
    13.5MB per image
  Compressed:
    Up to 15x compression
    <1MB per image

## Slide 38: Communications Systems
Thumbnail generation:
  Bit depth: 12 bit  8 bit jpeg
  Reduce number of columns/rows by a factor (0.1)
12 bit jpeg, 1941 kB, FOV = 47
8 bit jpg, 4kB, FOV = 47

## Slide 39: Communications Systems
Hardware:
  Ukpik 1 Transceiver:
    Endurosat Type II UHF transceiver
    GMSK + FSK modulation
    Data rate: 1.2 kbps - 19.2kbps
    Half duplex
    Frequency range: 430-440MHz
    Output Power: 1W
    Noise Figure (LNA + filter insertion loss): 1.5dB

## Slide 40: Communications Systems

## Slide 41: Communications Systems
Hardware:
  Ukpik 1 Antenna:
  GOMspace 70 cm band Omnidirectional UHF CubeSat antenna
  Frequency range: 435
  LCHP forwards, RHCP backwards
  Peak gain 1.6dBi
  50
  30 g weight

## Slide 42: Communications Systems
Radiation Pattern Analysis:
  Information from GOMspace datasheet at 45

## Slide 43: Communications Systems
Work done by Kelsey Doerkson:
Additional information:
  Will be referring to monopole orientations in positive angle offsets.
  Referencing the substrate below
Datum

## Slide 44: Communications Systems
More information:
  45 degree offset of my model is more omnidirectional than ANT430 model from GOMspace
  The model makes an assumption of using perfect conductors for the monopoles
  Next steps: Add in the CubeSat structure to see the effects on the radiation pattern
  Bending was not done because it is unrealistic in ANSYS HFSS. Hands on testing more suitable

## Slide 45: Communications Systems
0 degrees:
  Max gain: 3.9 dB
  Min gain: -0.006dB

## Slide 46: Communications Systems
45 degrees:
  Max gain: 2.2 dB
  Min gain: -9.05dB

## Slide 47: Communications Systems
90 degrees:
  Max gain: 0.23dB
  Min gain: -0.007dB

## Slide 48: Communications Systems
Summary Chart for all monopole offsets simulated:
Monopole Offset (Degrees) | Maximum Gain (dB)
0 | 3.90
10 | 3.37
20 | 3.23
30 | 3.07
40 | 2.89
45 | 2.20
50 | 2.15
60 | 1.69
70 | 1.28
80 | 0.74
90 | 0.23

## Slide 49: Communications Systems
Groundstation Block Diagram
  Important Design Choices still:
    Filter design by capstone students
    Power amplifier gain
    Driven by: Third harmonic Output
    SDR transceiver specs.
      Etus USRB B210
    Link budget Output power need

## Slide 50: Communications Systems
Tight filtering needed
Moderate filtering needed

## Slide 51: Communications Systems
Link Budget:

## Slide 52: Communications Systems

## Slide 53: Communications Systems

## Slide 54: Communications Systems

## Slide 55: Communications Systems
Uplink Eb/No method chosen because SNR method has lacking information at this point of time.
Advice from Peter Kazakoff + outlined issues of Link Budget from July 31st 2019.
  Separating TX & RX when building ground station block diagram.
  Scaled back power from transmitter on earth
  Antenna noise temperature
    Adjusted CubeSat Noise temperature to gain-weighted average using ITU recommendations.

## Slide 56: Communications Systems
Antenna Noise Temperature:
  Ground station antenna still needs to be looked at. Conservative value of 530k chosen.
Cable loss was too high before, this has been scaled back to 0.85dB based on LM400 and 9m length.
Filter insertion losses added as an estimate 1 dB was added
Polarization switch was added in case of ADCS failure.

## Slide 57: Communications Systems
Frequency Licensing:
  Dr. Jayshri Sabarinathan and Nicholas Mitchell will be getting their amateur radio licenses.
  Required for RAC endorsement application
    Has been started but not completed
  Required for IARU satellite coordination request
    Has been started but not completed
  It is acknowledged that this will be the highest priority once PDR is over.

## Slide 58: Mechanical System
Work done by Claire Lizotte, 2018/2019 Capstone Teams
Work Presented by Bryan Southwell
Notes: Antenna release on the solar panels

## Slide 59: Mass Budget Margin Philosophy
10% Off the Shelf
15% Modified off the shelf
20% Custom Build
20% Supplier not determined

## Slide 60: Mass Budget
Subsystem | Mass (g) | Margin | Mass w/ Margin (g)
Mechanical |  |  | 
Structure | 1064 | ~17% | 1246
Thermal | 50 | 20% | 60
Deployment | 25 | 20% | 30
Electrical |  |  | 
EPS w/ Battery | 292 | 10% | 
Solar Panels | 388 | ~14% | 441
Custom Boards | 352 | ~17% | 409
ADCS | 140 | ~18% | 165
OBC | 56 | 10% | 64
COMMS | 178 | ~12% | 200
NISA Cameras | 300 | 10% | 330
Engraving | 150 | 20% | 180
TOTAL | 2997 | ~15% | 3446

## Slide 61: Deployment Mechanisms
Holes for plunger switches
Have not yet identified source for plunger switches

## Slide 62: Deployment Mechanisms
Burn wire for antennae

## Slide 63: Revised CubeSat Structure From MCR
Structure redesigned from the rails in
Each rail is similar yet unique to accommodated various components

## Slide 64: Revised Structure: Cover Plates
Separate parts from rails; bolted to rails
Relation between rail ends and top of camera lens. There must be at least 2 mm, as specified by Nanoracks.

## Slide 65: Revised Structure: Cover Plates
Cover plate with allowance for GPS antenna

## Slide 66: Revised Structure: Antenna, Rails and Cover Plate
The cover plate is transparent. The blue circles show where the antenna slots into the rails. The red circles show that the tabs that hold the cover plate onto the rails are on the opposite side of the corners from the antenna itself.

## Slide 67: Revised Structure: Antenna, Camera and Cover Plate
The antenna has a coaxial cable that plugs in where the red circle is.

## Slide 68: Revised Configuration
Black = camera
Turquoise = antenna
Light blue = transceiver
Pink = OBC
Tan = NAC engraving
Yellow = magnetorquers
Red = gyroscope
Light purple = custom board
Purple = GPS transceiver
Green = EPS with battery

## Slide 69: Revised Configuration: Custom Board 1
Magnetorquers are yellow. Connectors grey. Gyroscope block is red.

## Slide 70: Revised Configuration: Custom Board 2
The magnetorquer is yellow. The GPS transceiver is darker purple. the board is light purple. The connectors are grey.

## Slide 71: Manufacturing Strategy
Component | Manufacturing Method | Reasoning
Mounting Plates | Laser cut, then sheet metal bending | It is easier and quicker to laser cut the thin material
Rails | Milling | The mounting holes for the plates must be in specific locations
Cover plates | Milling | They cannot be laser cut due to the different depths.
Solar panel plates | Laser cut | Preliminary

## Slide 72: Assembly Strategy
Mount components to mounting plates

## Slide 73: Assembly Strategy
Layer the stack:
  Antenna
  Cover plate
  Prepare bolts

## Slide 74: Assembly Strategy
Layer the stack:
  Camera
  Transceiver

## Slide 75: Assembly Strategy
Layer the stack:
  OBC
  NAC engraving

## Slide 76: Assembly Strategy
Layer the stack:
  Custom Boards
  Connectors

## Slide 77: Assembly Strategy
Layer the stack
  Camera
  Cover plate

## Slide 78: Assembly Strategy
Mount the panels
Restrain the antenna

## Slide 79: Notes on Assembly
Cover plates to be revised to place GPS antenna cutout at same end as antenna
Actual antenna are longer for 2U
  CAD files from 1U antenna

## Slide 80: Thermal Analysis
Detailed thermal analysis and testing on this most recent model is subject of a Mechanical and Materials Engineering capstone project
Detailed simulation and testing results expected by March 2020

## Slide 81: Break For Lunch

## Slide 82: Electrical Power System
Work performed by Stephen Amey, Bryan Southwell, 2018/2019 Capstone Teams
Presented by Stephen Amey

## Slide 83: EnduroSat EPS + Batteries

## Slide 84: Power Interfaces

## Slide 85: EPS – Power generation subsystems
The Endurosat EPS provides Maximum Power Point Tracking (MPPT) via dedicated solar panel connectors.
The Endurosat EPS also provides monitoring and status readouts of each solar panel connected via its USB connector.
The Cubesat batteries are integrated within the Endurosat EPS.

## Slide 86: Nominal Power Budget
Subsystem | Component | Power [mW] | Time [h] | Energy [mWh]
COMMS | Transceiver | 82.5 | 0.85 | 70
OBC | On-Board Computer | 700 | 0.85 | 594
ADCS | Magnetorquer x3 | 600 | 0.85 | 509
 | Gyroscope x3 | 12 | 0.85 | 10
Payload | camera x2 | 3000 | 0.00 | 0
EPS | EPS Board | 75 | 0.85 | 64
Power Production | Solar Panels (Production) | 5631 | 0.85 | 4786
 |  | Consumed | + 20% | 1500
 |  | Produced | - 30% | 3350

## Slide 87: Transmitting Mode Power Budget
Subsystem | Component | Power [mW] | Time [h] | Energy [mWh]
COMMS | Transceiver | 1362 | 0.15 | 173
OBC | On-Board Computer | 700 | 0.15 | 105
ADCS | Magnetorquer x3 | 600 | 0.15 | 90
 | Gyroscope x3 | 12 | 0.15 | 2
Payload | camera x2 | 3000 | 0.00 | 0
EPS | EPS Board | 75 | 0.15 | 11
Power Production | Solar Panels (Production) | 3940 | 0.15 | 590
 |  | Consumed | + 20% | 457
 |  | Produced | - 30% | 413

## Slide 88: Imaging Mode Power Budget
Subsystem | Component | Power [mW] | Time [h] | Energy [mWh]
COMMS | Transceiver | 82.5 | 0.001 | ~1
OBC | On-Board Computer | 700 | 0.001 | ~1
ADCS | Magnetorquer x3 | 600 | 0.001 | ~1
 | Gyroscope x3 | 12 | 0.001 | ~0
Payload | camera x2 | 3000 | 0.001 | 3
EPS | EPS Board | 75 | 0.001 | ~0
Power Production | Solar Panels (Production) | 5631 | 0.001 | 5.6
 |  | Consumed | + 20% | 5.4
 |  | Produced | - 30% | 3.9

## Slide 89: Eclipse Power Budget
Subsystem | Component | Power [mW] | Time [h] | Energy [mWh]
COMMS | Transceiver | 82.5 | 0.35 | 29
OBC | On-Board Computer | 700 | 0.35 | 245
ADCS | Magnetorquer x3 | 600 | 0.35 | 210
 | Gyroscope x3 | 12 | 0.35 | 4
Payload | camera x2 | 3000 | 0.00 | 0
EPS | EPS Board | 75 | 0.35 | 26
Power Production | Solar Panels (Production) | 0 | 0.35 | 0
 |  | Consumed | + 20% | 617
 |  | Produced | - 30% | 0

## Slide 90: EPS: Inhibits
The kill switch inhibits function similarly to the RBF switch.
The Endurosat EPS provides dedicated connectors for kill switches 1 and 2.
The Endurosat EPS will power up the Cubesat when at least 1 of 2 kill switches is released (along with the RBF switch removed).
The 30-minute delay required for ISS deployments will be handled by a timer circuit that will be activated by the kill switches.

## Slide 91: Solar Panel: RBF, Jumpers and Bypass

## Slide 92: Solar Panel: RBF, Jumpers and Bypass

## Slide 93: Solar Panel: JTAG and OBC Bypass

## Slide 94: Solar Panel: JTAG and OBC Bypass

## Slide 95: Solar Panel: Accelerometer Bypass

## Slide 96: Solar Panel: Accelerometer Bypass

## Slide 97: EPS – Inhibits
Once 30 minutes have elapsed, the circuit will then allow the EPS to power up via its kill switch connectors.
If the JMP1 pins are inserted on the solar panel (and thus the EPS as well), the 30-minute timer should be disabled. This allows the Cubesat to be quickly powered up or down for testing via the RBF switch.

## Slide 98: EPS –30-minute timer
The 30-minute timer will be an intermediate step between the kill switches and the EPS kill switch connectors.
Upon kill-switch release, the 30-minute timer will begin.
After 30 minutes have elapsed, there will be a ‘closed circuit’ between the two respective pins of the kill-switch connectors.
Once this closed circuit is formed, if the RBF switch has been removed, then the Cubesat will be able to power on.

## Slide 99: EPS – RBF
The RBF switch is an audio-jack connector, creating a closed circuit when inserted.
This switch will interface directly with the Endurosat EPS, via its dedicated RBF switch connector. It will not interface with the 30-minute timer.
The functionality of the RBF switch will differ when the JMP1 connector is used. This will disable the self-locking functionality of the EPS, and will power down the Cubesat when the RBF pin is inserted. If JMP1 is not used, inserting the RBF pin WILL NOT power down the Cubesat.

## Slide 100: EPS – Jumper pins
The JMP1 and JMP2 connectors of the Endurosat EPS will be exposed via connectors on the solar panels, and provide additional functionality.
The JMP1 connector will – when a closed circuit between the pins is formed – disable the self-locking functionality of the EPS, allowing it the Cubesat to power off when the RBF pin is inserted (whereas if JMP1 is not connected, it will not power off if the RBF pin is inserted).

## Slide 101: EPS – Jumper pins
The JMP2 connector – when a closed circuit is formed between the pins – will allow for the batteries of the EPS to be charged via the EPS USB connector.
The EPS USB connector is exposed via the solar panels, and can be used for monitoring and control of the EPS, and charging the batteries when the JMP2 pins are connected together.

## Slide 102: EPS – Power generation subsystems – Solar cell layout
The solar cells selected are AZUR SPACE 3G30A solar cell assemblies.
4 solar cells will be used per panel, and with a collection of 4 panels, a total of 16 solar cells will be used.

## Slide 103: Solar Panel Assembly: Mounting Components
Electrical testing of all components should be performed and ensure they meet the standards specified in their respective datasheets.
Examine the surface of the PCB for any defects in the panel surface.
Clean the PCB and ensure it is free of debris.
Insert any components that are to lie embedded in the PCB’s surface (USB connectors, RBF switch, etc.) and properly stake them to the PCB.
Mount the photodiode base and antenna release to the PCB.
Mount the appropriate electrical components to the PCB in their designated locations.
Mount the appropriate connectors on the top and bottom sides of the PCB.
Perform testing of all electrical components of the panel thus far (antenna release, sensors, bypasses, RBF switch, solar cell circuit), and ensure they are all working as intended.

## Slide 104: Solar Panel Assembly: Preparing the Solar Cells
Inspect the solar cells for defects, cracks, stress marks etc. Set any such cells aside.
Ensure the interconnects are flattened.
Clean the cell and ensure it is free of debris.
Prepare a strip of silver foil.
Bond the strip to the designated location on the bottom-side of the cell (positive terminal) using silver epoxy. The strip should be exposed in the +Z direction of the solar cell.
Allow it to cure at 80°C for 3 hours.
Modify (cut or bend in a triangle shape) the connectors and silver foil to the appropriate lengths as required by the PCB solder points.

## Slide 105: Solar Panel Assembly

## Slide 106: Solar Panel Assembly: Laying Down Cells
Place the solar cell template on the NuSil tape, and cut around the template with the Exacto blade. Ensure there are no tears. The cutout should cover the entirety of the area given by the template. The template should also allow for venting space around the silver foil connector on the bottom-side of the cell as shown in Figure 28.
Clean the surface of the PCB with solvent and flux remover to ensure there is no debris. Perform the final cleaning with isopropyl alcohol.
Place the cutout of the NuSil tape over the marked position for the solar cell on the PCB to verify that it covers the entire area.
Remove the covering on the NuSil tape that will be attached to the PCB.
Apply the NuSil tape by allowing one tip of the tape to contact the board, then slowly rolling the rest down. Apply pressure to ensure no air is trapped underneath.
Verify that the NuSil tape has been laid down properly. If not, remove it and clean the area, then repeat the application until correct.
Clean the bottom of the solar cell (positive terminal) with isopropyl alcohol and ensure no debris remains.

## Slide 107: Solar Panel Assembly: Laying Down Cells
Remove the top covering of the NuSil tape to expose the adhesive.
Allow one tip of the solar cell to contact the adhesive, and slowly lay the cell down to avoid the trapping of air, while NOT applying pressure. Ensure that the cell is properly lined up before attempting, as it cannot be removed afterwards.
Starting at the end initially attached, use a credit card-like material to apply pressure and move towards the other side to attempt to remove any trapped air.
Inspect the bond to ensure it is complete and that there are no air bubbles present.
Trim any excess NuSil tape with the Exacto blade.
Repeat for the remainder of the solar cells.
Upon application of the final cell, perform testing to ensure the energy output of the solar panel meets the specified values.

## Slide 108: EPS – Test plan and test specifications
Develop the test plan and test specifications of the electrical subsystems
Testing plans in place for the solar panels as they are built. Their final tests are ensuring sensor circuits work as expected, and that it produces the specified max power under a known intensity.
Other tests should include EPS/OBC USB bypass, EPS jumpers, self-lock disable, and charging. Also include accelerometers, since all of these are on the solar panels.

## Slide 109: Attitude Determination and Control System
  Work performed by Andrew Ning, 2018/2019 Capstone Teams
  Work presented by Andrew Ning

## Slide 110: Nominal Attitude Configuration
Camera payload and UHF communications do not impose strict pointing requirements
Coarse pointing towards sun for power generation

## Slide 111: ADCS Hardware Suite
Sensors
Photodiodes (22)
Solar Panels (4)
3-Axis Magnetic Compass (1)
3-Axis Gyroscope (1)
Temperature Sensors
Actuator
3-Axis Magnetic Torque Rods

## Slide 112: Attitude Determination Overview

## Slide 113: Translation of Sensor Input to Usable Information
Photodiodes/Solar Panels
Sun sensors proven to be too costly
Sun sensor functionality will be fulfilled by photodiodes and solar panels

## Slide 114: Translation of Sensor Input to Usable Information
3-Axis Magnetic Compass
Measures Earth magnetic field in body frame
Earth magnetic field in inertial frame given by World Magnetic Model
3-Axis Gyroscope
Measures angular velocity in body frame
Integrated for angular distance (used when neither photodiode nor magnetic field information is available

## Slide 115: State Estimation
State estimation done with Multiplicative Extended Kalman Filter (MEKF)
Modified to be iterative in the form of a sequential MEKF (SMEKF)
Photodiode Normal Vectors
Attitude Error
Gyroscope Bias
Photodiode/Solar Panel Calibration Factor
Parameterized with Gibbs Error Vector
Bias along each axis
Measure of
Parametrized with azimuth () and elevation () angles
State Vector

## Slide 116: Albedo Filter
Filtering of albedo is done through the MEKF
Calibration factor also fulfills purpose of in-orbit photodiode calibration
Incoming light assumed to be in form of:
Measurement Matrix (Photodiode/Solar Panel Input)
Sensitivity Matrix (Photodiode/Solar Panel Input)

## Slide 117: Albedo Model
Reflectivity data based on NASA Total Ozone Mapping Spectrometer (TOMS)
Earth irradiance for each cell modeled as:
is the area of each cell (calculated using surface integral)
and are position vectors calculated with GPS readings
is the reflectivity of cell with latitude and longitude taken from TOMS data
Calculated for cells visible by both Sun and satellite

## Slide 118: MEKF Initialization
The internal attitude reference is initialized using TRIAD
Reference-Measurement Pairs
Sun Vector
  Body Frame: Vector created from photodiode/solar panel input
  Inertial Frame: Vector created from Sun and CubeSat position in inertial frame
Magnetic Field Vector
  Body Frame: Magnetic field vector measured with 3-axis magnetic compass
  Inertial Frame: Magnetic field vector modeled using World Magnetic Model based on current CubeSat position

## Slide 119: Attitude Determination Performance
Preliminary attitude determination design is modeled in MATLAB
Attitude error settles to average error of 2.86 degrees over 1 to 2 minute period
Performance can be improved with better tuning
Performance meets attitude requirements but can be improved with better tuning of parameters

## Slide 120: Attitude Control Overview
Detumbling is accomplished with B-dot control law
Large angle maneuvers are accomplished with PD control
Special situations in which angular velocity is large is mitigated with B-dot control law as well

## Slide 121: Attitude Control: Orbit Insertion
A B-dot bang-bang controller variant is used that produces a magnetic moment of
Preliminary results indicate approximate time of 4 orbital periods (8 hours) to reduce angular rate from 5 degrees per second in each axis to less than 0.1 degrees per second in each axis

## Slide 122: Attitude Control: Orbit Insertion

## Slide 123: Attitude Control: Slew
Large angle maneuvers done with PD control using eigenaxis rotation for shortest path
Control torque vector given by:
Where is the skew-symmetric matrix
J is the inertia matrix of the CubeSat
D and K are constant gain matrices
is the error vector between initial and desired attitude

## Slide 124: Attitude Control: Slew
Preliminary results indicate average of 15 seconds to perform re-orientation with error of less than 2-5 degrees achievable depending on tuning parameters
Performance is improvable with implementation of more robust controllers such as PID and

## Slide 125: Attitude Control: Slew

## Slide 126: Command and Data Handling
Work done by Alexis Pascual, 2018/2019 Capstone Teams
Work presented by Stephen Amey

## Slide 127: Command and Data Handling System
Endurosat OBC
ARM Cortex M4 (180Mhz)
2MB Program Memory Size, 256kB RAM, 2MB Flash Memory
SD Card Mount
JTAG port for umbilical interfacing during AIT Phase
PC 104 Connector
Picoblade - 12 Pin connector
TLE-110-01-G-DV – 20 Pin Connector
Molex 53398-0471 – 4 Pin connector
Hardware Configuration

## Slide 128: Command and Data Handling System
Component | Protocol | Physical Pin Connection
EPS Board Data | UART | PC104 (H1: 39, 40)
Solar Panels | SPI | 12 Pin (PAN: 5,6,9,10)
Transceiver | UART | PC104 (H1: 33, 35)
Gyroscope | SPI | 12 Pin (PAN: 5,6,9,10)
Magnetorquer | PWM | 12 Pin (PAN: 1,2)
Payload | USB | USB/P1
Interfaces

## Slide 129: Command and Data Handling System
Bootloader must be able to load the appropriate program image into the program memory.
Bootloader must be able to check integrity of program memory as well as RAM
Bootloader must be able to recover from software faults
Bootloader must be able to communicate with the ground station to receive updated program image packets
Bootloader must be able to assess the integrity of each packet before writing them into the flash memory
Bootloader must be able to assess the integrity of the whole program image
Bootloader must be able to write the program image into the program memory
Bootloader must be able to jump into the program memory to begin operations
Bootloader Philosophy

## Slide 130: Command and Data Handling System
Bootloader Philosophy

## Slide 131: Command and Data Handling System
Bootloader Philosophy

## Slide 132: Command and Data Handling System
Bootloader Philosophy

## Slide 133: Command and Data Handling System
Bootloader Philosophy

## Slide 134: Command and Data Handling System
Software will be developed on top of FreeRTOS
Language: C
RTOS Tasks and function calls will be designed around operation modes.
OBC by default will be on Nominal Mode, and background functions will monitor sensor outputs and command queues.
Interrupt Service Routines will be executed based on sensor output threshold and time-tagged commands.
Task priorities have are yet to be determined.
Software Development Approach

## Slide 135: Command and Data Handling System
Software Development Approach

## Slide 136: Command and Data Handling System
Software Development Approach

## Slide 137: Command and Data Handling System
Software Development Approach

## Slide 138: Command and Data Handling System
Prototyping Boards
Nucleo F429ZI
STM32 MCU
Cortex M4 (180Mhz)
192KB RAM
UART: 6
SPI: 5
Analog Input: 19
Flash Memory: 2MB
FreeRTOS capable

## Slide 139: Command and Data Handling System
One prototyping board will be used to develop bootloader and flight software.
The other prototyping board will be used to create a tester which will simulate sensors and other subsystems.
Tester will monitor flight software responses to sensor/subsystem input
Prototyping Boards

## Slide 140: Command and Data Handling System
Tests conducted to simulate the most resource intensive task using 3 Nucleo-F429ZI prototyping boards
Image of size 13.5MB was successfully passed from the “camera” to the OBC over UART
Image was then deconstructed and passed over to the “transceiver” module over UART
Image was successfully reconstructed by the “transceiver” module
Estimated Processing Load

## Slide 141: Command and Data Handling System
The tests prove that the hardware configuration (i.e. CPU, RAM, I/O) can handle the most resource intensive task of receiving an image from the camera and passing it to the transceiver module.
Additional tests need to be conducted to determine CPU time, power consumption, and memory allocation for all operating modes.
Future tests include adding a transmitter module on the prototyping boards to simulate actual operations
Estimated Processing Load

## Slide 142: AIT
Presented by Nick Mitchell

## Slide 143: AIT
EGSE:
  Multimeters
  Power Supplies
  SDR MegaBee for rapid prototyping
  Oscilloscopes
  Network Analyzer
  Spectrum Analyzer
  Waveform Generators
  Microscopes
  Soldering stations (with multiple tips and necessary equipment from CSA workshop)

## Slide 144: AIT
Goal: Design the equipment and software needed to test a CubeSat / FlatSat with little human interaction.

## Slide 145: AIT
Testing:
  Acknowledged that antenna release mechanism testing is critical*
  It also has moving parts and will require some human interaction for verification that it will NOT damage the surrounding components.
  Heavy emphasis on testing starting mechanism when designed for maximum safety assurance*
  The other components will be designed to be modularly tested.

## Slide 146: AIT
Red = Will Become Flight Hardware
Black = Can be cheaply prototyped (not flight hardware right away)

## Slide 147: AIT
EGSE:
  SDR Transceiver (USRP B210 if available)
  SDR Transceiver (MegaBEE cube)
    70MHz-6GHz
    56MHz bandwidth per channel
    23dBm output Power
    -94dBm receiver sensitivity level
    Software: HDL,Matlab/Simulink,C/C++/Python
    USB V2.0 connection
    SMA antenna connectors
    FREE, Already in lab (good for rapid prototyping)
Notes: Note that the USRP is going to be purchased but that will not stop our prototyping! I have asked jayshri and we are able to make use of the MegaBEE cube that we have in lab (we have other SDR’s as well)

## Slide 148: AIT
CubeSat Test Plan:
  Safety and Handling Procedures:
    BBM:
      Summer student work 2019 + Capstone 2018 prelim
    Demonstration model:
      FlatSat
    Structural and Thermal Model:
      Bus redesigned, Need to do another thermal + vibe test
    Proto-Flight Model:
      FlatSat will turn into it
    Flight Model:
      From Proto-Flight Model

## Slide 149: AIT
People Resources:
  CubeSat Club members during the year.
    Will be started this year!!
    Safety training, bringing up to speed on project
    Assembly and Integration training
    Extra hands on demonstration model under team leads
  Capstone Teams:
    Structural and Thermal model
    Groundstation design
    PCB Design for custom boards
      Including inspection protocols, manufacturing plan and testing plan

## Slide 150: AIT
People Resources:
  Team Leads:
    Individual subsystems
    Develop a detailed testing plan if not done already.
  Summer Students(2019):
    Documentation is done (Github and Sharepoint)
    Assembly instructions for CubeSat bus
    Assembly instructions for assembling solar panels

## Slide 151: AIT
Still to do:
  EMI testing plan, requirements and procedure
    Identify resources required
  Custom board design + testing
  Request For Deviation form for early turn on of camera
    Timer circuit based on above decision
  Antenna release mechanism and testing
  Operations protocols and training with CubeSat club students

## Slide 152: AIT
Laboratory Environments for Spacecraft Assembly:
What class of clean room necessary?
Is air handling necessary?
Options for rooms:
  Thomson Engineering Building room 6
  Optics Lab Spencer Engineering Building room 3025A
  Western NanoFabrication Facility

## Slide 153: Programmatics
Outreach Update
Status Updates
Budget Update
Risk Assessment

## Slide 154: Outreach Updates
Revised plans with NAC
Institute for Earth and Space Exploration (Western Space)
CubeSat Club
Space Business Case Competition
Educational Kits

## Slide 155: Budget Update
Current procurement estimates in line with budget
To-date prototyping in line with budget
Nunavut travel re-aligned for more frequent travel of Western members to NAC

## Slide 156: Status Updates
1St draft of SDP and BOM to CSA
RF Comms licencing pending
RSSSA licencing pending

## Slide 157: Programmatic Risk Assessment
Risk ID | Description | Impact | Probability | Status Entry Date
1 | Cost of prototyping more than budgeted | 2 | 4 | January 10, 2019
2 | Cost of flight model more than budgeted | 4 | 3 | January 10, 2019
3 | HQP turnover leads to gaps in experience and capability | 4 | 4 | January 10, 2019
Notes: Matt B?

## Slide 158: Programmatic Risk Assessment
Programmatic Risk Matrix |  |  |  |  |  |  | 
LIKELIHOOD | 5 |  |  |  |  |  | 
 | 4 |  | 1 |  | 3 |  | 
 | 3 |  |  |  |  |  | 
 | 2 |  |  |  | 2 |  | 
 | 1 |  |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5 | 
 |  | IMPACT |  |  |  |  | 
Notes: Matt B?

## Slide 159: Technical Risk Assessment
Risk ID | Description | Impact | Probability | Status Entry Date
1 | UHF Communication Licensing | 5 | 2 | January 10, 2019
2 | Earth Observation Licensing | 3 | 3 | January 10, 2019
3 | Payload Camera | 5 | 1 | January 10, 2019
4 | Solar Panels assembly | 5 | 3 | January 10, 2019
5 | Ground Station Development | 3 | 3 | January 10, 2019
6 | Antenna Deployment Development | 5 | 2 | October 10, 2019
7 | Deployment Switch / Circuit Development | 5 | 2 | October 10, 2019
8 | Magnetorquer Development | 2 | 3 | October 10, 2019
9 | Software Development | 4 | 3 | October 10, 2019
Notes: Matt B?

## Slide 160: Technical Risk Assessment
Technical Risk Matrix |  |  |  |  |  |  | 
LIKELIHOOD | 5 |  |  |  |  |  | 
 | 4 |  |  |  |  |  | 
 | 3 |  | 8 | 2,5 | 4,9 |  | 
 | 2 |  |  |  |  | 1, 6 ,7 | 
 | 1 |  |  |  |  | 3 | 
 |  | 1 | 2 | 3 | 4 | 5 | 
 |  | IMPACT |  |  |  |  | 
Notes: Matt B?

## Slide 161: Thank you